UNIVERSITY OF THE WEST INDIES

CAVE HILL CAMPUS

Department of Computer Science, Mathematics & Physics

# ELET1110 (EL10B) -  Digital Electronics

# Class Test 2						     		    Thursday, April 3, 2014

- Give the binary string for both the next number and the previous number in the Gray Code

10111										[2]

- How many flip-flops will be complemented when the counter below is incremented

1011101111										[1]

- Show by means of a timing diagram how a glitch could occur at the output of a NOR

gate when the input changes for 01 to 10							[3]

- Implement the following function using a 3 x 8 decoder and one additional logic gate

[4]

- Implement the following function using an 4 x 1 multiplexer

[4]

- 10011011 is passed through a parity generator and the output is a 1. Is this EVEN or ODD

Parity system ?										[1]

EITHER DO  QUESTION 7  OR  QUESTION 8   BUT NOT BOTH

- A 3-bit finite state device, built with J-K flip flops, has the following flip-flop input functions

Draw the State Diagram									[6]

What are the unused states ?									[3]

Is the device self correcting ?									[1]

- A 3-bit finite state device, built with J-K flip flops, has the following repeating sequence

1,3,0,4,6,2…...

Find the simplified flip flop input functions							[10]