UNIVERSITY OF THE WEST INDIES

CAVE HILL CAMPUS

Department of Computer Science, Mathematics & Physics

# ELET1110(EL10B) -  Digital Electronics

# Class Test 2									Monday, November 5, 2012

- Show by means of a timing diagram how a glitch could occur at the

output of a two input NOR gate when the input changes from 01 to 10					[3]

- Each bit in a binary word is stored in a flip-flop, how many flip-flops

will be complemented  when the number below is incremented

00101011											[1]

- Implement the function below with an 4 x 1 multiplexer

[4]

- Implement the following function using a 3 x 8 decoder (ACTIVE LOW) and one logic gate

[4]

- Give the binary string for both the next number and previous number in the Gray Code

10101											[2]

- 10010101 is passed through a parity generator and output is 1. EVEN or ODD parity system ?	[1]

EITHER DO QUESTION 7 OR QUESTION 8 BUT NOT BOTH

- A 3-bit finite state device, built with J-K flip-flops, has the following flip-flop input functions.

Draw the State Diagram											[6]

What are the unused states ?										[3]

Is the device self-correcting?										[1]

- A 3-bit finite state device, built with J-K flip flops, has the following repeating sequence

1,6,7,2,4…..

Find the simplified flip flop input functions								[10]