THE UNIVERSITY OF THE WEST INDIES

EXAMINATIONS   OF  MAY   2015

## Code and Name of Course: ELET3120 (EL31L) – COMMUNICATION CIRCUITS

Date and Time:                             	                                Duration: 2 hours

INSTRUCTIONS TO CANDIDATES:  This paper has  2  pages and  5  questions.

Answer any   THREE (3)   of   FIVE (5)   questions.

Question 1:

With the aid of a diagram explain the principle of an Absorption Modulator and state its advantages and disadvantages when compared to other AM modulation techniques.	[7]

Describe what factors must be considered in choosing an IF frequency.			[4]

With the aid of diagrams, show what is meant by “percentage of modulation”

and describe what factors must be considered in choosing a percentage.			[5]

Briefly explain why it would be desirable to suppress the carrier in AM and how

suppression is achieved											[4]

Question 2:

##### Draw a schematic of a ratio detector and explain it’s operation.					[6]

Draw a block diagram of an FM receiver that uses a Squelch control and explain its

use.														[6]

Explain the relationship between phase modulation and frequency modulation

and show how one may be obtained from the other.						[6]

Why are frequency multipliers used in FM transmitters ?						[2]

PLEASE TURN OVER

The University of the West Indies					Course Code: ELET3120

_______________________________________       _________________________________

DO NOT WRITE OR TYPE ON THE BACK OF THIS SHEET:  USE ONE SIDE ONLY

INSTRUCTIONS:  Each page must be signed by the FIRST AND SECOND EXAMINERS.

......................................... 			............................................

First Examiner				  			Second Examiner

Date: 2015/03/							Date: 2015/03/

#### Page 2

Question 3:

- Draw a block diagram of a digital television (DTV) and explain it’s operation	[8]

- Explain why the HSL color model is used in television and describe how it is

implemented in NTSC and PAL.								[6]

- Explain, with the aid of diagram(s), the operation of a sync separator circuit	[6]

Question 4:

( a )	Explain the term “parasitic oscillation” and discuss its causes, effects and

avoidance in the design of extremely high frequency circuits				[6]

( b )    Show how advances in semiconductor technology and precision engineering

have made higher oscillator frequencies a modern reality				[7]

( c )	Describe the various sources of noise that affect communications systems

and indicate how these may be reduced or eliminated.					[7]

Question 5:

( a )	Compare and contrast “balanced” and “unbalanced” transmission line		[6]

( b )	Explain what is meant by ground, space, and sky waves. Which of these waves

are used for transmitting signals in the bandwidth .05 MHz - 1.5MHz, and

88 – 108 MHz.											[6]

( c )	Design a 5-element Yagi (half-wave dipole) antenna cut for a center frequency		of 100MHz. Show spacings used.								[8]

# END   OF   QUESTION   PAPER

The University of the West Indies					Course Code: ELET3120

_________________________________________________       _______________________

DO NOT WRITE OR TYPE ON THE BACK OF THIS SHEET:  USE ONE SIDE ONLY

INSTRUCTIONS:  Each page must be signed by the FIRST AND SECOND EXAMINERS.

......................................... 			...........................................

First Examiner							Second Examiner

Date: 2015/03/							Date: 2015/03/