# ELET3120 Communications Circuits CLASS TEST 2  Friday, April 5, 2013

- Briefly describe the function of the following devices as they relate to

television equipment:  (a) Diplexer (b) Sync Separator (c) Matrix		[6]

- With the aid of a diagram explain the difference between frequency

inversion and  frequency conversion					            [4]

3.  Compare the advantages and disadvantages of

the ratio detector and the Foster-Seeley detector 				[4]

4.   What two methods can be used to extend the range of VHF and higher

frequency communications beyond the radio horizon ?				[2]

5. What is the most important advantage of a log-periodic antenna ?		[1]

6. Name two examples of a driven array.						[2]

7.What is the most significant advantage of a driven array over a parasitic

array ?										[2]

8. If the input impedance of an antenna is 300 ohms and it is fed by a

75 ohm unbalanced transmission line, what is the SWR on the line ?		[1]

9. What determines the characteristic impedance of a transmission line ?		[2]

10. What are two causes of fading in radio communications ?			[2]

11. List the four variations of the ionosphere and their causes			[8]

12. In a direct FM transmitter, what happens to the frequency deviation when:

(a) the amplitude of the modulating signal is increased			[2]

(b) the frequency of the modulating signal is decreased			[2]

13.  What was undesirable about the Armstrong oscillator that caused Hartley to

design his oscillators ?								[2]

14.What is the advantage of the shunt-fed Hartley over the series-fed

Hartley.										[2]